## Slide 1: Smog
Dr Indranil Ghosh

## Slide 2: Introduction
During winter, under the very cold climatic condition the air layers at the ground level become too much cold and condensed to move upward and remain near the ground. Air from the upper layers, having a higher temperature, can not travel downward in such a situation. Such inversion of temperature is the first factor responsible for the formation of smog; the second factor is the mixing of the poisonous gases emitted from industries and motor vehicles with foggy air. Thus, fog and smoke combined together and form the smog.

## Slide 3: Types of Smog
There are two different type of smog –
Sulphurous Smog or classical smog or reducing smog.
Nitrogenous Smog or photochemical smog or oxidizing smog.

## Slide 4: Sulphurous Smog or Chemical smog or Reducing Smog
The mixture of smoke, fog and Sulphur dioxide form the Sulphourous smog. This smog affected London city badly for several centuries after the introduction of coal as fuel. So, this is also known as London smog. The mixtures of the components are chemically reducing in nature. Hence, they are also called as Reducing smog.

## Slide 5: Components of Sulphurous Smog
Oxide of Sulphur
Particulate matter which are coming from smoke
Humidity or water from fog.

## Slide 6: Process of formation of Sulphurous Smog
It occurs mainly in the early morning hours in winter where there is relatively high humidity. Air, near the ground is cooled by conduction from cooled surface, especially on a clear night. Higher up in the troposphere the air is not cooled appreciably. So in the absence of winds, warm air lies over the cooler air i.e., temperature inversion takes place. In this particular stable atmospheric zone (due to the temperature inversion) the following chemical reactions take place that lead to the formation of Sulphourous smog.

## Slide 8
The reaction (2) takes place in presence of sunlight & particulate matter. combines with moisture from fog to form Sulphurous acid . This acid is again oxidized to form Sulphuric acid and this combine with NH3 present in smoke to form ammonium salt.
This smog produces much more dangerous effects than the sum total of and particulars.
The chemical reactions in this type of smog are not photochemical in nature. Throat irritation is felt in this smog.

## Slide 9: Nitrogenous Smog or Photochemical Smog or Oxidizing Type
Nitrogenous smog is different from Sulphourous smog. It is not related to smoke or fog as well. The main component of this type of smog is oxides of Nitrogen. So it is called as Nitrogenous smog. During the formation of this type of smog photochemical reactions take place and so it is also called as photochemical smog. This type of smog first time took place at Los Angles and so it is also known as Los Angles type of smog.

## Slide 10: Components of Photochemical smog
Oxides of Nitrogen
Tropospheric Ozone
Hydrocarbon
Photo radiation

## Slide 11: Process of formation of nitrogenous or Photochemical smog
Reactive hydrocarbon from auto exhaust interact with tropospheric O3 to form free radical RCH2
RCH2 rapidly reacts with O2 to form another free radical RCH2O2
RCH2O2 reacts with NO to produce NO2 and free radical RCH2O
The new free radical then interacts with to yield a stable aldehyde (RCHO) and hydroperoxyl radical HO2
HO2 then reacts with another molecule of NO to give NO2 and RCH2O
HO is extremely reactive and rapidly reacts with the stable hydrocarbon RCH3 to yield HO2 and regenerate RCH2 ,thereby completing cycle.